CMPUT313-LAB2
By James Devito

1.1 - Introduction

In this experiment we are testing the stop and wait protocol, the purpose of this experiment is to obtain results found in simulation and compare them with expected results by mathematical model. For this experiment we will be using the cnet simulator the protocol is stopandwait and our topology files consist of 4 different topologies as followed

- NETa : The length of each application layer message is 2000 bytes, and the physical layer does not corrupt or lose frames.
- NETb : The length of an application layer message is a uniform random variable with value between 2000 bytes and the default maximum length, and the physical layer does not corrupt or lose frames
- NETc : The length of each application layer message is 2000 bytes, and the physical layer does not lose frames, but corrupts only data frames (that is, ACK frames are delivered reliably) with probability 0.5 each.
- NETd : The length of each application layer message is 2000 bytes, and the physical layer does not lose frames, but corrupts both data and ACK frames with probability 0.5 each.
1.2 - Experimental Obersvations and Data

1.2 - Experimental Obersvations and Data Continued

Problems

  - Mathematical Model

First let's define
- Transmission Rate = R
- Transmission time of a packet = Tpkt
- Message Rate = Rmsg
- Propagation Delay = Tprop
- Size of a packet = L
- Round Trip Time = RTT
Common Calculations

R = 56kbps
L = 2000 bytes
Rmsg = 1000ms
Tprop = 2500ms

Threrrorfree = 1 / (Tpkt + RTT)
Thr = Thr-errorfree / Nr
Where Nr is the average number of times the protocol retransmits

Tpkt = L/R
Tpkt = 2000bytes/56kbps
Tpkt = 0.2857 s

RTT = 2 * (Tprop) + Rmsg
RTT = 6000ms

Please assume these calculations to be common to each test unless stated otherwise

NETa
In the case of NETa there is no error generation so our throughput will be error free
Using the above values we find : Thr-errorfree = 1 / (Tpkt + RTT) = 0.1590 pkts/sec
Each packet is 2KB so,
Thr-errorfree = 0.1590 pkts/second * 2KB/pkt = 0.318 KB/sec = 0.32 KB/sec
and Thr-messages = 0.1590 msg/sec = 0.16 msg/sec

NETb
In the case of NETb there is no error generation so our throughput will be error free
L-min = 2000 bytes
L-max = 8000 bytes
L is a uniform random variable and can be expressed as L = (L-min + L-max)/2
L = ( 2000 + 16000 ) / 2 = 9000 bytes

Therefore Tpkt = L/R = 5000 bytes / 56 Kbps
Threrrorfree = 1 / (Tpkt + RTT) = 0.1372 pkt/sec
Similarl to NETa (9KB per packet) Thr = 1.235KB/sec = 1.23 KB/sec
Thr-messages = 0.1372 msg/sec = 0.13 msg/sec

NETc
In the case of NETc there is error generation

Using common values we find : Thr-errorfree = 0.1590 pkt/sec
There is only 1 source of error so Nr = 1 / (1 – Pframecorrupt)
Therefore Thr = 0.1590 / (1 / (1 – 0.5))

Giving us a result of Thr = 0.0795 pkt/sec
Each packet is 2Kb
Therefore Thr = 0.09925 pkt/sec * 2KB/pkt = 0.159 KB/sec = 0.16KB/sec
and Thr-messages = 0.0795 msg/sec = 0.08 msg/sec

NETd
In the case of NETd there is error generation in the form of lost and corrupt frames
let Pframecorrupt be P = 0.5
Pframeloss be Q = 0.5

Using common values we find : Thr-errorfree = 0.1590 pkt/sec

In this case there are 2 sources of error so we must first find our Nr
Nr =
Nr =

Therefore Thr = (Thr-errorfree / Nr) = 0.1590
Thr = pkt/sec
Each packet is 2kb
Therefore Thr = pkt/sec * 2KB/pkt = KB/sec

1.3 Results

For NETa
Expected: Thr-data = 0.32 KB/sec	Experimental Result : Thr-data = 0.31 KB/sec
: Thr-msg = 0.16 msg/sec	: Thr-msg = 46 msg/ 300 sec = 0.15 msg/sec

% Error – Thr-data = | ( (Thr-data(found) – Thr-data(expected) ) / Thr-data (expected) ) | * 100
        = ( ( 0.31 – 0.32) / 0.32 ) * 100 = 3.1%

similarly % Error Thr-msg = 6.6%

In the case of NETa our experiment results are within an acceptable error range of our expected results. This
confirms that are calculations were acceptably correct.

For NETb
Expected: Thr-data = 1.23 KB/sec	Experimental Result : Thr-data = 1.94 KB/sec
: Thr-msg = 0.13 msg/sec	: Thr-msg = 35 msg/ 300 sec = 0.12 msg/sec

% Error formula similar to NETa section
% Error – Thr-data = 60.16%

similarly % Error Thr-msg = 7.69%

In the case of NETb the error for our estimation of message throughput falls within acceptable error, however in
this case we have observed a large error in the throughput for the data, but this is acceptable because in the case
of this experiment the design parameter of the size of the message was set to a uniform random variable between	2000 bytes and 16000 bytes. Considering this it is expected that our observed error falls relatively close to 50%.

For NETc
Expected: Thr-data = 0.16 KB/sec	Experimental Result : Thr-data = 0.13 KB/sec
: Thr-msg = 0.08 msg/sec	: Thr-msg = 21 msg/ 300 sec = 0.07 msg/sec

% Error formula similar to NETa section
% Error – Thr-data = 18.75%

similarly % Error Thr-msg = 12.5%

In the case of NETc we observe a slightly larger error when comparing our expected values and our experimental
values. This is likely because of the introduction of random error generation, this will cause different runs to
potentially have different end values. I believe if we were to run the simulation for longer or ran the simulation
many times we will see a decrease in our error

2. STOP-AND-WAIT Protocol on Path Networks